## Slide 1: Hopfield Net Based Neural Processor
Kamalakkannan Kamalavasan
Yasas Seneviratne
Dr. Ajith Pasqual

## Slide 2: Introduction
Neural net processing in a single core processor takes a considerable amount of time.
To overcome this using the Graphics Processing Unit(GPU) is a commonly used alternative in general purpose applications.
But in the field of embedded processing and Application Specific Integrated Circuits(ASICs) GPUs are rarely or not at all used which makes the processing of neural net based computations inefficient and time consuming.
Hopfield net is a Recurrent Neural Network(RNN) which is capable of identifying a pre trained pattern and uses minimum number of multiplications as compared to Convolutional Neural Networks(CNN).
This is why Hopfield net was used as the base for the development of the Neural net processor which is capable of working alongside a conventional embedded or ASIC processor.

## Slide 3: Architecture : Overview
The figure shows a processor which is miniaturized for the simplicity of explanation.
Processor consists of the following main components.
  The Processing Elements
  The FIFO Array
  The Weight matrix
  The Final Calculator
  Controller

## Slide 4: Architecture : Processing Element
The Processing Element(PE) has two different states of operation in the training and recognition stages.
In the PE only addition and comparison operations are used.

## Slide 5: Architecture : Processing Element
The Processing Element(PE) has two different states of operation in the training and recognition stages.
In the PE only addition and comparison operations are used.
Multiplication by 1 and -1 are achieved by addition and 2’s complement addition.

## Slide 6: Stages of Operation: Training Stage 1
The 1st stage of training is generation of the weight matrix.
This process is fully parallelized.
The final generated values in the FIFOs are equivalent to the upper triangular sector values in the weight matrix.

## Slide 7: Stages of Operation: Training Stage 2
Moving the upper triangular sector of the weight matrix in to the shift register array and completion of the matrix

## Slide 8: Stages of Operation: Detection

## Slide 9: Stages of Operation: Detection

## Slide 10: Fields of Application
Handwriting recognition
Feature detection in images
License plate identification
Road sign detection

## Slide 11: Simulation Specifications
Catagory | Neural Net Processor | Microblaze Processor | NNEP
Development Board | Xilinx Zybo (xc7z010clq400-1) | Xilinx Zybo (xc7z010clq400-1) | Custom Chip
Operating frequency | 100MHz | 1200MHz | 400MHz
Simulation Methodology
Simulation was done using a test bench which used text files as inputs.
One input files contained the pattern to be taught to the Neural net processor and the other contained the pattern to be recognized.
The test bench reads the files accordingly in each state of operation.
The Neural net processor is also capable of running at 200MHz

## Slide 12: Results : Performance vs Microblaze
Chart: Average training time(ns)
| Training
Microblaze | 768000
Neural Net Processor | 530
Chart: Average recognition time(ns)
| Recognition
Microblaze | 1847600
Neural Net Processor | 530

## Slide 13: Results : Performance vs NNEP
Chart: Throughput GOPs
| Throughput
NNEP(200MHz 16 PEs) | 6.275
Neural Net Processor(100MHz) | 1.6
Neural Net Processor(200MHz) | 3.2

## Slide 14: Results : Resource Utilization
Site Type | Used | Fixed | Available | Utilization%
Slice LUTs | 1026 | 0 | 17600 | 5.83%
LUT as Logic | 948 | 0 | 17600 | 5.39%
LUT as Memory | 78 | 0 | 6000 | 1.30%
Slice Registers | 2074 | 0 | 35200 | 5.89%
Register as Flip Flop | 2074 | 0 | 35200 | 5.89%

## Slide 15: Results : Power
Results were generated at 30 degree Celsius.
Total on chip power | 0.111W
Dynamic | 0.005W
Signal | 0.002W
Logic | 0.002W
IO | <0.001W
Static | 0.106W
Junction Temperature | 31.3 Celsius

## Slide 16: Shortcomings
Limitation of the Hopfield algorithm which made it only possible to train a limited number of patterns to a given number of nodes. If the number of nodes were N number of patterns that can be taught equaled 0.15*N.
Weight matrix size increases with additional number of nodes with this the number of processing elements and other resource utilization increase.

## Slide 17: Further Improvements
Usage of the same processing elements to compute a larger weight matrix based Hopfield computation(Access sharing).
Development of a NOC or a bus architecture for reducing the number of connections required.
Use of a memory to store multiple Weight matrices making it possible to detect additional patterns.
Making the core capable of storing any number of patterns trained to it.